Summary of the

SPECIFICATIONS FOR COMPETITION EQUIPMENT

(Alpine racing skis – Racing suits - Crash helmets)

Edition 2016/17 (Juli 2016)

All equipment used by Athletes is governed by the FIS Specifications for Competition Equipment.

http://www.fis-ski.com/mm/Document/documentlibrary

# - Restrictions - WC/WSC/OWG/COC/UNIVERSIADE/YOG

| Ski length: (Minimum) 1.2.1.1 | Ladies - Downhill - Ladies - Super-G - Ladies - GS - Ladies - SL - Men - Downhill - Men - Super-G - Men - GS - Men - SL - | 210 cm** 205 cm** 188 cm** 155 cm 218 cm** 210 cm** 193 cm** 165 cm * | Important! The ski length must be marked on the ski!!! Ski length measurement tolerance of +/- 1 cm ** -5 cm tolerance for FIS * Men U18 (first year) at FIS -10cm tolerance |
| --- | --- | --- | --- |
| Profile width under Binding: 1.2.1.2.1 | DH-SG-GS Ladies & Men - SL - Ladies & Men - | <=65 mm >=63mm | Min. width of the running surface under the binding and in front of the binding without any tolerance! |
| Profile width in front of Binding 1.2.1.2.2 | DH-SG - Ladies & Men - GS - Ladies - GS - Men - SL - Ladies & Men - | <=95 mm <=103 mm <=103 mm nl |  |
| Radius (Minimum): 1.2.1.3 | DH - Ladies & Men - Super-G - Ladies - Super-G - Men - GS - Ladies - GS - Men - SL - Ladies & Men - | Min. 50 m Min. 40 m Min. 45 m Min. 30 m Min .30 m nl | The radius must be marked on the ski! Radius measurement for DH skis with a preparation tolerance of -1 m |
| Max. Standing height (ski/plates/binding) 2.1.2 | Ladies & Men | Max 50 mm | Distance between the bottom of the running surface of the ski and the ski boot sole without any tolerance! |
| Ski boots 3.2 Thickness of ski boot soles | Ladies & Men | Max 43 mm | Distance between the ski boot sole and the base of the heel including all hard and soft parts |
| Racing suits 5. – 5.1 | Competition suits used in DH, SG and GS must have a minimum air permeability of 30 litres per m2/sec (with a tolerance of 3,0 litres per m2/sec) The competition suits must be equally porous in all parts, both from the outside in and from the inside out. Label and plomb systems, will be valid during the transition period until the end of the 2017/18 season. | For GS/SG/DH label attesting conformity with FIS specifications, affixed at the back of the lower left leg above the top of the ski boot cuff area of the competition suit is compulsory. |  |
|  |  |  | Label attesting conformity with FIS specifications for Alpine competition suits: Minimum Width: 30mm Minimum Height: 45mm |  |
| Crash helmets 6. – 6.2.3 | The use of crash helmets is compulsory at all FIS alpine ski events. For SL helmet model to be certified under EN 1077 or ASTM 2040 as minimum standards. NB1: Soft ear padding is allowed NB2: crash helmets fulfilling higher safety standards can be used a fortiori in SL | For GS/SG/DH label attesting conformity with FIS specifications, affixed in a visible location at back of the helmet is compulsory. |  |
|  |  |  | Label attesting conformity with FIS specifications for Alpine racing helmets: Minimum Width: 10mm Minimum Height: 15mm |  |

FIS Equipment Controller

Herbert Klammer

Mobile: +393470864248

klammer@pass.dnet.it